# SECTION 09840

PERFORATED METAL ACOUSTICAL CEILING TILES

PART 1 GENERAL

  - SECTION INCLUDES

    - Sound Absorptive Wall Panels

    - Sound Absorptive Ceiling Panels [Clouds]

    - Sound Absorptive Ceiling Tile

    - Miscellaneous Accessories

  - REFERENCES

    - ASTM International:

      - ASTM C423 Standard Test Method for Sound Absorption and Sound Absorption Coefficients by the Reverberation Room Method.

      - ASTM E84 Standard Test Method for Surface Burning Characteristics of Building Materials.

      - ASTM E795 Standard Practices for Mounting Test Specimens During Sound Absorption Tests.

  - SYSTEM DESCRIPTION

    - Performance Requirements:

      - Surface Burning Characteristics ASTM E84 Class I

  - SUBMITTALS

    - General: Submit listed submittals in accordance with Conditions of the Contract and Division 1 Submittal Procedures Section.

    - Product Data: Submit product data sheet, for specified products.

    - Shop Drawings: Submit shop drawings showing layout, edge profiles and panel components, including anchorage, accessories, finish colors and textures.

    - Samples: Submit selection and verification samples of finishes, colors and textures.

    - Test Reports: Certified test reports showing compliance with specified performance requirements.

  - DELIVERY, STORAGE & HANDLING

    - General: Comply with Division 1 Product Requirements Section.

    - Delivery: Deliver materials in manufacturer’s original, unopened, undamaged containers with identification labels intact.

    - Storage and Protection: Store materials protected from exposure to harmful environmental conditions and at temperature and humidity conditions recommended by the manufacturer.

  - PROJECT CONDITIONS

    - Environmental Requirements: Do not install panels until building has been enclosed and environmental conditions approximate interior conditions that will exit during occupancy.

# PART 2 PRODUCTS

| 2.01 | A. | MANUFACTURERS Acceptable Manufacturer: Sound Seal, Inc., located at 50 HP Almgren Drive, Agawam, MA 01001. Contact |
| --- | --- | --- |
|  |  | Sound Seal Architectural Division at 413-78-1770, Email: soundquality@soundseal.com; Web: www.soundseal.com |
|  | B. | Substitutions: No substitutions permitted. |
| 2.02 |  | LAY-IN ACOUSTICAL CEILING TILES |
|  | A. | Acoustic Tiles: Sound Seal SERENITY Metal Absorptive Ceiling Tiles |
|  |  | Tile Thickness: 1 inch (25.4 mm) or 2 inches (50.8 mm) Tile Size: To fit standard ceiling for 24 inches (607 mm) x 24 inches (607 mm) grid and 24 inches (607 mm) x 48 inches (1214 mm). Specify either 9/16” or 15/16” suspended grid style. |
|  | B. | Panel Performance: |
|  |  | 1. Sound Absorption: Provide panels that are certified to meet the following minimum sound absorption |
|  |  | coefficients when tested in accordance with ASTM C423 and E 795: |
|  |  | 1 inch Thick Tile: |
| 125 Hz: | 0.11 |
| 250 Hz: | 0.28 |
| 500 Hz: | 0.68 |
| 1000 Hz: | 0.90 |
| 2000 Hz: | 0.93 |
| 4000 Hz: | 0.96 |
| NRC: | 0.70, minimum |
| 2 inch Thick Tile: |  |
| 125 Hz: | 0.17 |
| 250 Hz: | 0.86 |
| 500 Hz: | 1.14 |
| 1000 Hz: | 1.07 |
| 2000 Hz: | 1.02 |
| 4000 Hz: | 0.98 |
| NRC: | 1.00, minimum |

      - Fire: Provide panels when tested in accordance with ASTM E84 demonstrate: Flame Spread = 10, Smoke Developed=10.

- Tile Construction:

  - All materials to be electro galvanized / galvanealed steel.

  - Tile body shall be fully formed one piece perforated metal shell. Material shall be minimum 22 gauge (.76 mm) steel sheet perforated with 3/32 inch (2 mm) diameter holes on 5/32 inch (4 mm) staggered centers for a 33% open area.

  - Edge Style:  Specify square lay-in or Tegular edge style.

- Acoustical Insulation: Fill shall be [1 inch (25.4 mm)] or [2 inch (50 mm)] thick fiberglass or mineral wool having a density of not less than 1.5 pounds per cubic foot (24 kg/cubic m). When required, panel fill shall be totally encased in a 2 mil thick heat sealed black poly wrap

- Finish:  Baked polyester powder coat.

# PART 3 EXECUTION

  - EXAMINATION

    - Examine surfaces to receive acoustical tiles. Do not begin installation until any unsatisfactory conditions have been corrected.

  - INSTALLATION

    - Install tiles into suspended ceiling grid in locations and in patterns as indicated on the drawings.

    - Install each tile in accordance with manufacturer’s instructions using approved anchors and fasteners.

  - CLEANING

    - Follow manufacturer’s instructions for cleaning tiles soiled during installation. Replace tiles that cannot be cleaned to as new condition.

    - Keep site free from accumulation of waste and debris.

# END OF SECTION